## Slide 1: NCHRP 14-42: Determining the Impact of Connected and Automated Vehicle Technology on State DOT Maintenance Programs
The National Cooperative Highway Research Program (NCHRP) is sponsored by the individual state departments of transportation of the American Association of State Highway and Transportation Officials. NCHRP is administered by the Transportation Research Board (TRB), part of the National Academies of Sciences, Engineering, and Medicine, under a cooperative agreement with the Federal Highway Administration (FHWA). Any opinions and conclusions expressed or implied in resulting research products are those of the individuals and organizations who performed the research and are not necessarily those of TRB; the National Academies of Sciences, Engineering, and Medicine; the FHWA; or NCHRP sponsors.

## Slide 2: NCHRP 14-42: Determining the Impact of Connected and Automated Vehicle Technology on State DOT Maintenance Programs
Project Summary
March 2024
Shauna Hallmark, Omar Smadi, Jon Markt, Eric Plapper, Paul Carlson, Katie Zimmerman and Greg Duncan

## Slide 3
Project Objectives
Identify connected and automated vehicle (CAV) assets used by agencies (State DOT, Cities, Counties)
Identify likely maintenance needs for those assets
Develop successful strategies related to maintenance
Assess the workforce implications
Image source: Shutterstock

## Slide 4: Survey of State and Local Agencies
Survey of agency current/planned use of CAV assets which targeted:
  State DOTs
  Smart cities
53 participants from 39 states (no local agencies)
  Responses for each state were combined
Around 40% have added, increased, modified or removed assets to address CAV
Planned
Current

## Slide 5: Changes to Communication/Data
The most common change is the addition of dedicated short-range communications (DSRC) or increasing communication capacity.
Image source: Shutterstock
Current
Planned

## Slide 6: Changes in Assets
Most common change is addition of or changes in traffic signal controls or an increase in cameras
Planned
Current

## Slide 7: Changes in Pavement Markings
The most common change is the addition of high-contrast or durable markings
8% removed Botts Dotts
Image source: www.3m.com/3M/en_US/
road-safety-us/applications/road-markings/
Planned
Current

## Slide 8: Changes in General Assets
The most common change is the addition/modification of roadway weather information system (RWIS) and electric vehicle infrastructure
http://www.westcoastgreenhighway.com/
Planned
Current

## Slide 9: Changes in Maintenance Practices
Various changes planned
More frequent maintenance
New practices
Additional inspection, etc.
Image source: Shutterstock

## Slide 10: Targeted Interviews
Focused on 4 assets
  Roadside units (RSU)
  Onboard units (OBU)
  Pavement markings
  Infrastructure based camera for AV applications
Interviews with 10 DOTS (CA, CO, FL, GA, KY, MI, MN, NV, NH, WA)
Interviews with 3 agencies (Las Vegas, Tampa Hillsborough Expressway Authority, Columbus)
Interviews with 6 asset vendors
Interviews with private highway maintenance contractors (Ferrovial Services, Roy Jorgensen, Louis Berger)

## Slide 11: Overall
Technologies are new and agencies have limited maintenance experience with CAV assets
Information from OEMs has not been transparent or consistent making it difficult to invest or set performance metrics
Technology is changing rapidly
Funding is often available to implement CAV assets but not to maintain
Many agencies rely on vendors for maintenance and support
CAV assets likely to increase maintenance needs

## Slide 12: Roadside Units
Provide wireless communication between roadside infrastructure and vehicles
Survey
  20 agencies have them
  19 agencies plan to add
Many agencies rely on private vendors or original maintenance contracts
Typical maintenance
  Monitoring
  Software-related maintenance
  Ensure access to power
www.traffictechnologytoday.com

## Slide 13: Roadside Units
Common failure issues
  Weather
  Security credentialing
  Improper installation
Maintenance challenges
  Sparse communication in rural agencies
  Ability to determine whether RSUs are functioning
  Time-consuming over-the-air updates

## Slide 14: On-board Units
Vehicle-based equipment that can communicate with RSUs or other ITS infrastructure
Applications
  Most common – snowplows
  Bus priority
  Traffic signal timing
Most agencies did not have much experience with maintenance, however OBUs are a mature technology
https://grandavebridge.codot.gov/projects/snowplowsignalpriority.

## Slide 15: On-board Units
Typical maintenance
  Software-related maintenance
  Checking cables/sensors
Maintenance challenges
  Sparse communication in rural agencies

## Slide 16: Pavement Markings
Indicate forward alignment for AV
Proposed standards
  6-inch for higher speed roadways
  Chevrons in gore areas
  Dotted extension through exit ramp
High-contrast markings also used
Survey
  26 added/increased/modified markings for AV
Hansra 2016
Paul Carlson, Texas A&M Transportation Institute (TTI).

## Slide 17: Pavement Markings
Typical maintenance
  Increases cost of painting
  None indicated increased restriping due to AV
Maintenance challenges
  No retro-reflectivity or other maintenance standards have been established
https://ogs.ny.gov/greenny/pavement-marking-paint

## Slide 18: Camera-Based Pedestrian and Bicycle Detection
Used to identify the presence of vulnerable road users
System can provide info to surrounding vehicles through vehicle to infrastructure (V2I)
Survey (question was about cameras for CAV in general)
  11 added/increased/modified use of cameras
  20 plan to add/increase/modify the use of cameras
General Maintenance needs for ped/bike detection
  Regular cleaning particularly in adverse weather situations
  Checking placement
  Checking cables
Maintenance Standards
  None specific to CAV applications
https://transit-signal-priority.medium.com/

## Slide 19: Other Assets/Information
Focused Phase II efforts on previous assets
Summarized available maintenance information for 6 additional assets
  Signs
  Traffic signal controllers
  RWIS
  Additional communication capacity
  Machine-readable signs
  Data and digital infrastructure
https://climateillinois.wordpress.com/

## Slide 20: Workforce Needs
Summarized agency workforce concerns
The current mix of skills within the DOT workforce is not oriented toward technology
Position classifications and pay ranges are not sufficient for recruiting and retaining needed new talent
Internal training programs to develop skills within the current DOT workforce are needed or have not yielded the expected benefits
Many states are currently using contractors to maintain CAV equipment
Agencies noted uncertainty about the adoption timelines of technology and the absence of guidance from OEMs makes planning future investments difficult