## Slide 1: Appendix J: HCM: Urban Streets Weaving Analysis Method
Highway Capacity Analysis
NCHRP 15-66: Operational Performance and Safety Effects
of Arterial Weaving Sections
September 2023

## Slide 2: Outline
Overview of the HCM 7th Edition’s “Urban Streets Segment Analysis” method.
Overview of the HCM’s proposed method on “Arterial’s Weaving Operational Performance” based on NCHRP 15-66
Case Study #1, Settlers Blvd in Round Rock, TX; Assessing the impact of channelized right turn on urban street segment performance due to weaving
Case Study #2, Y Freedom Dr, Charlotte, NC; Assessing the impact of an access point on urban street segment performance due to weaving
Safety Analysis of Arterial Weaving Segments
Conclusions and Take Aways
HCM: Urban Street Weaving Method

## Slide 3: About the HCM
Overseen by TRB committee on Highway Capacity and Quality of Service (hcqstrb.org)
Most methods are developed via national level projects such as NCHRP Projects*.
Four Volumes:
  I. Concepts
  II. Uninterrupted Flow
  III. Interrupted Flow
  IV. Applications Guide (Online only)
HCM OVERVIEW
(*) NCHRP: National Cooperative Highway Research Program

## Slide 4: Urban Street Segments HCM Chapter 18 Based on the 7th Edition of Highway Capacity Manual (HCM7)

## Slide 5: Urban Streets Characteristics
URBAN STREETS - OVERVIEW
They are part of the “Interrupted Flow” methods
Traffic control devices creating delay
Stop signs, traffic signals, roundabouts
Traffic flow patterns inherent to control type
  Platoons of vehicles vs. random arrivals
Presence of pedestrians and bicycles also evaluated as part of interrupted flow methods

## Slide 6: Urban Streets Components
URBAN STREETS - OVERVIEW
Intersection 1
Intersection 2
Intersection 3
Segment 1
Urban Street Facility
Segment 2
Interchange

## Slide 7: Urban Streets Analysis
URBAN STREET SEGMENTS
Analysis boundaries include:
  Roadway right-of-way
  Operational influence area of each boundary intersection
Interdependent with operation at boundary intersections
Service Measure: Travel Speed (mi/h)
HCM Pages 18-4 & 18-5

## Slide 8: Volume Balancing
Entering and exiting volumes must be balanced for accurate analyses
Unbalanced volumes due to:
  Different counting times for boundary intersections
  Uncaptured midblock demand
  Counting inaccuracy
URBAN STREET SEGMENTS
HCM Exhibit 18-9 & 18-10
Entering volume:
200 + 1,000 + 100 + 50 = 1,350 veh/h
Exiting volume:
50 + 1,210 + 40 + 50 = 1,350 veh/h
=
Entering Volume
Exiting Volume

## Slide 9: Base Free-Flow Speed
URBAN STREET SEGMENTS
HCM Equation 18-3
Length of street with a restrictive median (raised curb)
Proportion of segment with curb on the right-side
Proportion of segment’s right-hand curb line with parking stalls (parallel or angle)
Manual calibration factor
Determined as function of segment geometric inputs:
Number of active access points (> 10 veh/h) on the right side of street
Manual input for additional mid-segment delay sources not addressed by HCM (e.g. mid-block pedestrian crossing)

## Slide 10: Base Free-Flow Speed
URBAN STREET SEGMENTS
HCM Equation 18-3
Speed constant
Determined as function of segment geometric inputs:

## Slide 11: Access Points
URBAN STREET SEGMENTS
HCM Equation 18-3
Can be modeled in Urban Streets
Inputs:
Turning movement demands
Number of lanes for each movement
PHF

## Slide 12: Definitions
Running Time
The time a vehicle spends in motion through the segment
Through delay
Control delay of the through movement in the boundary downstream intersection
Automobile Traveler Perception Score
Optional performance measure to indicate traveler’s perception of quality of service
URBAN STREET SEGMENTS

## Slide 13: Flow Profile
Applies for downstream signalized intersection only
Measures the proportion of traffic arriving downstream during green
Green part of the graph = vehicles arriving on green
  The higher the better
  Improves intersection uniform delay (d1)
URBAN STREET SEGMENTS
HCM Exhibit 18-9

## Slide 14: Platoon Dispersion Model
URBAN STREET SEGMENTS
Platoons from the upstream signal degrade while traveling the segment, due to differing speeds of vehicles
Arrival flow rate lower than discharge flow rate
HCM Exhibit 30-3

## Slide 15: Running Time
URBAN STREET SEGMENTS
HCM Equation 18-15

## Slide 16: Running Time
URBAN STREET SEGMENTS
HCM Equation 18-15
number of access point approaches on the right side in the subject direction of “ ravel (points)

## Slide 17: Travel Speed
URBAN STREET SEGMENTS
HCM Equation 18-15
About the through delay:
Computed with the signalized intersection methodology (Equation 19-18)
If through movement has shared lanes → Use Equation 18-10

## Slide 18: Level of Service
URBAN STREET SEGMENTS
HCM Exhibit 18-1
LOS | % of BFFS | Travel Speed Threshold by BFFS (mi/h) |  |  |  |  |  |  | Volume-to-Capacity Ratio*
 |  | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 
A | > 80% | >44 | >40 | >36 | >32 | >28 | >24 | >20 | ≤ 1.0
B | 67-80% | >37 | >34 | >30 | >27 | >23 | >20 | >17 | 
C | 50-67% | >28 | >25 | >23 | >20 | >18 | >15 | >13 | 
D | 40-50% | >22 | >20 | >18 | >16 | >14 | >12 | >10 | 
E | 30-40% | >17 | >15 | >14 | >12 | >11 | >9 | >8 | 
F | < 30% | ≤17 | ≤15 | ≤14 | ≤12 | ≤11 | ≤9 | ≤8 | 
F | any | any |  |  |  |  |  |  | > 1.0
Service measure: Travel Speed (mi/h) as a percentage of base free-flow speed (BFFS)

## Slide 19: Limitations
URBAN STREET SEGMENTS
HCM Page 18-13
Significant Grade along the Link
Cyclic Queue Spillback (queue grows and discharges at every cycle)
Cross-street Congestion Blockage
Bicycles in Traffic Stream

## Slide 20: Required Input Data
URBAN STREET SEGMENTS
HCM Exhibit 18-5
Required Data and Units | Potential Data Source(s) |  | Suggested Default Value
Traffic Characteristics Data |  |  | 
Demand flow rate by movement group at boundary intersection (veh/h) | Field data, past counts | Field data, past counts | Must be provided
Access point flow rate by movement group (veh/h) | Field data, past counts | Field data, past counts | See discussion in text
Midsegment flow rate (veh/h) | Field data, past counts | Field data, past counts | Estimate using demand flow rate at the downstream boundary int. approach

## Slide 21: Required Input Data
URBAN STREET SEGMENTS
HCM Exhibit 18-5
Required Data and Units | Potential Data Source(s) |  | Suggested Default Value | 
Geometric Data |  |  |  | 
Number of lanes by movement group at boundary intersection | Field data, aerial photo | Field data, aerial photo | Must be provided | Must be provided
Upstream intersection width (ft) | Field data, aerial photo | Field data, aerial photo | Must be provided | Must be provided
Segment approach turn bay length at boundary intersection (ft) | Field data, aerial photo | Field data, aerial photo | Must be provided | Must be provided
Number of midsegment through lanes | Field data, aerial photo | Field data, aerial photo | Must be provided | Must be provided
Number of lanes at access points – segment approach | Field data, aerial photo | Field data, aerial photo | Number of through lanes on approach = number of midsegment through lanes No right-turn lanes If median present, one left-turn lane per approach; otherwise, no left-turn lanes | Number of through lanes on approach = number of midsegment through lanes No right-turn lanes If median present, one left-turn lane per approach; otherwise, no left-turn lanes
Number of lanes at access points – access point approach | Field data, aerial photo | Field data, aerial photo | One left-turn and one right-turn lane | One left-turn and one right-turn lane
Segment approach turn bay length at access points (ft) | Field data, aerial photo | Field data, aerial photo | 40% of the access point spacing, where spacing = 2 x (5,280)/Da in feet, but not more than 300 ft nor less than 50 ft | 40% of the access point spacing, where spacing = 2 x (5,280)/Da in feet, but not more than 300 ft nor less than 50 ft

## Slide 22: Required Input Data
URBAN STREET SEGMENTS
HCM Exhibit 18-5
Required Data and Units | Potential Data Source(s) |  | Suggested Default Value
Geometric Data, cont. |  |  | 
Segment (site) length (ft) | Field data, aerial photo | Must be provided | Must be provided
Restrictive median length (ft) | Field data, aerial photo | Must be provided | Must be provided
Proportion of segment with curb (decimal) | Field data, aerial photo | 1.0 (curb present on both sides) | 1.0 (curb present on both sides of segment)
Number of access point approaches | Field data, aerial photo | See discussion in text | See discussion in text
Proportion of segment with in-street parking (decimal) | Field data | Must be provided | Must be provided
Other Data |  |  | 
Analysis period duration (h) | Set by analyst |  | 0.25 h
Speed limit (mi/h) | Field data, road inventory |  | Must be provided
Performance Measure Data |  |  | 
Through control delay at boundary intersection (s/veh) | HCM method output |  | Must be provided
Through stopped vehicles at boundary intersection (veh) | HCM method output |  | Must be provided
2nd and 3rd term back-of-queue size for through movement at boundary intersection (veh/lane) | HCM method output |  | Must be provided
Capacity by movement group at boundary intersection (veh/h) | HCM method output |  | Must be provided
Midsegment delay (s/veh) | Field data |  | 0.0 s/veh
Midsegment stops (stops/veh) | Field data |  | 0.0 stops/veh

## Slide 23: New Method to Evaluate Operational Performance of Arterial Weaving Based on NCHRP Project 15-66

## Slide 24: Scope of Urban Streets Weaving Analysis Method
The new method accounts for weaving movements within each urban street link.
Based on the proposed method, two movements can create a weave maneuver in urban streets links:
  Right turn from access points into the link
  Right turn from unsignalized channelized right turn at the upstream intersection.
Proposed HCM Urban Streets Weaving Method

## Slide 25: Changes to the Urban Streets Core Methodology
Proposed HCM Urban Streets Weaving Method
  New Step 1.5 to estimate Turbulence Index and assess the weaving maneuver's impact
  Revised Step 2 to adjust the running time to account for the through delay due to weaving

## Slide 26: Step 1.5: Estimate Turbulence Index (TI)
Proposed HCM Urban Streets Weaving Method
The Turbulence Index (TI) is calculated to assess the degree of traffic turbulence caused by weaving movements:
= Turbulence index (in units of (veh/hr)2 / ft)
= The potential conflict opportunities for the weaving movement i considering the conflicting volume the movement must traverse to its destination
= Distance to stop bar for weaving movement i
= the Total number of weaving maneuvers within the weaving section (including weaving to and from mid-block access points)

## Slide 27: Step 1.5: Estimate Turbulence Index (TI)
Proposed HCM Urban Streets Weaving Method
The PCO for a given movement set is the product of the conflicting demands. Below is an example of a left turn at the downstream intersection originating from the access point and conflicting with the through traffic:
Where:
  = Flow (veh/h) arriving from the access point and making a left turn at the downstream intersection
  = Total flow (veh/h) arriving from the arterial
Illustration of Potential Conflict Points Opportunities for Movement VRL

## Slide 28: Step 1.5: Estimate Turbulence Index (TI)
Proposed HCM Urban Streets Weaving Method
The PCO must be computed for the following conflicting movements:

## Slide 29: Step 2: Include the Impact of Weaving in the Running Time
The new Through Delay due to Weave () term is included in the running time model:
Where:
Proposed HCM Urban Streets Weaving Method

## Slide 30: Implementation in the HCM’s STREETVAL Computational Engine
Proposed HCM Urban Streets Weaving Method
The proposed models and changes to the HCM core urban street methodology are implemented in the Excel-based STREETVAL V8.30.1
This computational engine can be used to evaluate the impact of arterial weaving in Urban Streets with Signalized Intersections.
Excel STREETVAL V8.30.1

## Slide 31: Implementation In the HCM’s STREETVAL Computational Engine
Proposed HCM Urban Streets Weaving Method
The proposed method does not require any additional information, i.e., no additional inputs are added to the STREETVAL.
However, the output page of STREETVAL shows all MOEs considering the new NCHRP 15-66 method.
Two additional MOEs are also reported in the STREETVAL 8.30.1:
  Turbulence Index (TI)
  Delay due to arterial weaving

## Slide 32: Case Study #1 Old Settlers Blvd, Round Rock, Tx Evaluate the impact of a weaving maneuver from upstream channelized right turn

## Slide 33: Old Settlers Blvd, Round Rock, TX
The WB direction of this arterial is impacted by a weaving maneuver from an upstream unsignalized channelized right turn.
The two arrows represent two movements that conflict with one another.
Case Study #1
N

## Slide 34: Old Settlers Blvd, Round Rock, TX
STREEVAL V 8.30.1 is used to model this urban street and estimate the impact of the weaving maneuver.
Site geometry is extracted from google maps
The turning volumes and signal timing are based on the data collected in this project but altered as needed to demonstrate the weaving impact.
We have used an earlier version of STREETVAL V8.30 to compare the impact of urban street weaving on key urban street performance measures.
For simplicity, the access points are not modeled in this case study to focus on the impact of the upstream unsignalized channelized right turn.
Case Study #1
Urban Street Evaluation |  |  |  |  |  |  |  |  | 
General Information |  |  |  |  |  |  |  |  | 
Location: | Round Rock, TX |  |  |  |  | Analysis period: |  | 7:15 am to 7:30 am | 
Agency: | University of Florida |  |  |  |  | Analysis year: |  | 2023 | 
Location: |  |  |  |  |  | Analyst: |  | Bob | 
Travel direction for Movement 2 at all intersections |  |  |  |  | EB | Area type: |  | Other | 
File name: | C:\Users\user1\Documents\NCHRP 15-66 Case Study TX |  |  |  |  |  |  |  | 
Number of analysis periods: |  |  |  |  | 1 |  |  |  | 
Basic Segment Information |  |  |  |  |  |  |  |  | 
Segment | Cross Street Names |  |  |  | Speed Limit, mph |  | Through Lanes |  | Segment
Number | Street to West |  | Street to East |  | EB | WB | EB | WB | Length, ft
1 | Chisholm Trail RD |  | I-35 Frontage RD |  | 40 | 40 | 2 | 2 | 700
2 | I-35 Frontage RD |  | Third Avenue |  | 35 | 35 | 2 | 2 | 1800
3 | Third Avenue |  | Fourth Avenue |  |  | 35 |  |  | 
4 | Fourth Avenue |  | Fifth Avenue |  |  |  |  |  | 
5 | Fifth Avenue |  | Sixth Avenue |  |  |  |  |  | 
6 | Sixth Avenue |  | Seventh Avenue |  |  |  |  |  | 
7 | Seventh Avenue |  | Eighth Avenue |  |  |  |  |  | 
8 | Eighth Avenue |  | Ninth Avenue |  |  |  |  |  | 
Cycle Length, s: |  | 100 |  |  | No. Intersections: |  | 2 | Total, mi: | 0.13

## Slide 35: Old Settlers Blvd, Round Rock, TX
Phase Configuration:
Lane Geometry:
Case Study #1
Chisholm Trail Rd
I-35 Frontage Rd

## Slide 36: Old Settlers Blvd, Round Rock, TX
Traffic Demand
Flow Rates (vph)
Case Study #1
Chisholm Trail Rd
I-35 Frontage Rd

## Slide 37: Old Settlers Blvd, Round Rock, TX
The arterial weaving maneuver takes place in the EB direction.
A Turbulence Index of 36 (veh/hr)^2/ft is achieved.
Delay due to weaving is estimated to be 4.3 seconds and added to the running time.
Accounting for the impact of the weave maneuver in the EB direction, changes the LOS from D to E.
Case Study #1
Key Urban Streets MOEs for EB Direction | Considering Delay due to Arterial Weave | Without Considering Delay due to Arterial Weave
Base Free-Flow Speed, mph | 41.41 | 41.41
Running Time, s | 18.95 | 14.52
Running Speed, mph | 25.18 | 32.87
Through Delay, s/veh | 11.51 | 11.373
Travel Speed, mph | 15.67 | 18.43
Stop Rate, stops/veh | 0.000 | 0.000
Spatial Stop Rate, stops/mi | 0.00 | 0.00
LOS | E | D
***NCHRP 15-66: TI | 38.21 | NA
***NCHRP 15-66: d_wv, sec | 4.43 | NA

## Slide 38: Case Study #2 Freedom Dr, Charlotte, NC Evaluate the impact of a weaving maneuver from an access point

## Slide 39: Freedom Dr, Charlotte, NC
The EB direction of this arterial is impacted by a weaving maneuver from an access point with high demand (243 vph).
The two arrows represent the two selected movements that conflict with one another.
Case Study #2
N

## Slide 40: Freedom Dr, Charlotte, NC
STREEVAL V 8.30.1 is used to model this urban street and estimate the impact of the weaving maneuver.
Site geometry is obtained from google maps
The turning volumes and signal timing are based on the data collected in this project but altered as needed to demonstrate the weaving impact better.
We have used an earlier version of STREETVAL V8.30 to compare the impact of urban street weaving on key urban street performance measures.
For simplicity, the access points are not modeled in this case study to focus on the impact of upstream unsignalized channelized right turn.
Case Study #2
Urban Street Evaluation |  |  |  |  |  |  |  |  | 
General Information |  |  |  |  |  |  |  |  | 
Location: | Charlotte, NC |  |  |  |  | Analysis period: |  | 7:15 am to 7:30 am | 
Agency: | University of Florida |  |  |  |  | Analysis year: |  | 2023 | 
Location: |  |  |  |  |  | Analyst: |  | Bob | 
Travel direction for Movement 2 at all intersections |  |  |  |  | EB | Area type: |  | Other | 
File name: | C:\Users\user1\Documents\NCHRP 15-66 Case Study NC |  |  |  |  |  |  |  | 
Number of analysis periods: |  |  |  |  | 1 |  |  |  | 
Basic Segment Information |  |  |  |  |  |  |  |  | 
Segment | Cross Street Names |  |  |  | Speed Limit, mph |  | Through Lanes |  | Segment
Number | Street to West |  | Street to East |  | EB | WB | EB | WB | Length, ft
1 | I-85 SPUI Interchange |  | Ashley Rd |  | 45 | 45 | 3 | 4 | 1200
2 | Ashley Rd |  | Third Avenue |  | 35 | 35 | 2 | 2 | 1800
3 | Third Avenue |  | Fourth Avenue |  |  | 35 |  |  | 
4 | Fourth Avenue |  | Fifth Avenue |  |  |  |  |  | 
5 | Fifth Avenue |  | Sixth Avenue |  |  |  |  |  | 
6 | Sixth Avenue |  | Seventh Avenue |  |  |  |  |  | 
7 | Seventh Avenue |  | Eighth Avenue |  |  |  |  |  | 
8 | Eighth Avenue |  | Ninth Avenue |  |  |  |  |  | 
Cycle Length, s: |  | 130 |  |  | No. Intersections: |  | 2 | Total, mi: | 0.23

## Slide 41: Freedom Dr, Charlotte, NC
Phase Configuration:
Lane Geometry:
Case Study #2
I-85 SPUI Interchange
Ashley Rd

## Slide 42: Freedom Dr, Charlotte, NC
Traffic Demand
Flow Rates (vph)
Case Study #2
I-85 SPUI Interchange
Ashley Rd

## Slide 43: Old Settlers Blvd, Round Rock, TX
The arterial weaving maneuver is present in the EB direction.
A Turbulence Index of 233 (veh/hr)^2/ft is achieved.
As such, the delay due to weaving is estimated to be 11 seconds and added to the running time.
Accounting for the impact of arterial weave maneuvers changes the LOS from B to D.
Case Study #2
Key Urban Streets MOEs for WB Direction | Considering Delay due to Arterial Weave | Without Considering Delay due to Arterial Weave
Base Free-Flow Speed, mph | 43.60 | 43.60
Running Time, s | 31.41 | 19.73
Running Speed, mph | 26.05 | 41.46
Through Delay, s/veh | 4.569 | 7.118
Travel Speed, mph | 22.74 | 30.47
Stop Rate, stops/veh | 0.000 | 0.000
Spatial Stop Rate, stops/mi | 0.00 | 0.00
LOS | D | B
***NCHRP 15-66: TI | 233.23 | NA
***NCHRP 15-66: d_wv, sec | 11.67 | NA

## Slide 44: Safety Analysis of Arterial Weaving Segments

## Slide 45: Safety Analysis of Arterial Weaving Segments
  Three types of safety analyses were conducted to identify the safety effects of varying geometric, volume, and traffic conditions in arterial weaving segments:
  Analysis of crash data for field study sites
  Analysis of conflict data for field study sites
  Analysis of conflict data from a driving simulator
  The goal was to:
  Identify key design and safety issues that could help agencies reduce crashes along arterial weaving segments
  Identify future research needs to develop methods that predict the safety performance of arterial weaving segments for inclusion in the AASHTO Highway Safety Manual (HSM)
NCHRP 15-66

## Slide 46: Definitions of Terms for Safety Analysis
NCHRP 15-66

## Slide 47: Results of Safety Analysis
NCHRP 15-66
  Results of safety analyses yielded expected results; although with a few exceptions, the parameters in the statistical models were not statistically significant:
  Field Study Sites:
    Analysis of crash data showed that as the ratio of the weave length to site length increases, the number of crashes decrease
    Analysis of conflict data showed that as the ratio of the weave length to site length increases, the number of heavy braking (HB) conflicts decrease
  Driving Simulator:
    Analysis of conflict data showed that as the site length increases, the number of time-to-collision (TTC) conflicts decrease

## Slide 48: Conclusions and Take Aways

## Slide 49: Conclusions and Take Aways
The NCHRP 15-66 proposed method is capable of assessing the impact of weave maneuvers originating from:
  Unsignalized channelized right turn from the upstream intersection
  Right turns from access points
NCHRP 15-66 uses a newly defined term, Turbulence Index (TI), to determine the presence of arterial weave impact on predicted HCM MOEs.
NCHRP 15-66 evaluates the impact of an arterial weave on the HCM Urban Street Method by estimating its effect on the segment running time.
NCHRP 15-66

## Slide 50: Conclusions and Take Aways
Based on testing the proposed method on two real work facilities in Texas and North Carolina, a significant change in the predicted MOEs found by accounting for the impact of the arterial weave.
When a channelized right turn in the upstream intersection or access points is present in the Urban Streets, it is recommended to use the proposed method within the HCM analysis to account for the potential impact of the arterial weave.
The NCHRP 15-66 research did not find any significant impact of weaving on other HCM Urban Streets performance measures such as the stop rate.
NCHRP 15-66

## Slide 51: Conclusions and Take Aways
Designers should determine if there is an opportunity to close/remove mid-block access points along arterial weaving segments
  Closing mid-block access points will eliminate weaving maneuvers and result in increasing the length of the weaving area along the segment
  This will likely reduce potential crashes that may be attributed to weaving maneuvers
Analysis of crash and conflict data yielded sufficient information to suggest that additional research to develop methods that predict the safety performance of arterial weaving segments would yield promising results
NCHRP 15-66

## Slide 53: The National Cooperative Highway Research Program (NCHRP) is sponsored by the individual state departments of transportation of the American Association of State Highway and Transportation Officials. NCHRP is administered by the Transportation Research Board (TRB), part of the National Academies of Sciences, Engineering, and Medicine, under a cooperative agreement with the Federal Highway Administration (FHWA). Any opinions and conclusions expressed or implied in resulting research products are those of the individuals and organizations who performed the research and are not necessarily those of TRB; the National Academies of Sciences, Engineering, and Medicine; the FHWA; or NCHRP sponsors.